## Slide 1: PiBot
Building and programming

## Slide 2: Process
Unpack all components
Component check
Voltage Divider on PCB
Power rails
  Positive +5V
  Negative – common throughout
I2C rails
  SDA
  SCL

## Slide 3: I2C Setup
sudo raspi-config
  I2C enable
  Reboot
lsmod | grep i2c
  Check if two files are listed
sudo apt-get install i2c-tools
  i2cdetect –y 1
  Check for any I2c addresses and take note
sudo apt-get install libi2c-dev
sudo pip3 installsmbus2

## Slide 4: Using LCD with i2c

## Slide 5: Motor Driver

## Slide 6
In 1 = GPIO14 (8)
In 2 = GPIO15 (10)
EnA = GPIO18 (12)
In3 = GPIO23 (16)
In 4 = GPIO24 (18)
EnB = GPIO25 (22)

## Slide 7: Motor Driver Tasks
Make Motor A turn
  Fwd, Rev and change speed L, M, H.
Add second Motor B
  Make both run: Fwd, Rev, speed, L, M, H
Make Motor A and Motor B turn in opposite directions.
  i.e. Add two options turn robot left and turn robot right
On the LCD
  Display the action of the motor
  Display speed of motors.

## Slide 8
5v
Gnd
SDA
SCL